## Slide 1: EE359 – Lecture 10 Outline
Average Ps (Pb)
MGF approach for average Ps
Combined average and outage Ps
Ps due to Doppler ISI
Ps due to ISI

## Slide 2: Review of Last Lecture
Linear modulation more spectrally efficient but less robust than nonlinear modulation
Ps approximation in AWGN:
Probability of error in fading is random
  Characterized by outage, average Ps, combination
Outage probability
  Probability Ps is above target; Probability gs below target
Fading severely degrades performance
Ps
Ps(target)
Outage
Ts
t or d
  Used when Tc>>Ts

## Slide 3: Average Ps
Expected value of random variable Ps
Used when Tc~Ts
Error probability much higher than in AWGN alone
Alternate Q function approach:
  Simplifies calculations (Get a Laplace Xfm)
Ps
Ps
Ts
t or d

## Slide 4: Combined outage and average Ps
Used in combined shadowing and flat-fading
Ps varies slowly, locally determined by flat fading
Declare outage when Ps above target value
Ps(gs)
Pstarget
Ps(gs)
Ps(gs)
Outage

## Slide 5: Doppler Effects
High doppler causes channel phase to decorrelate between symbols
Leads to an irreducible error floor for differential modulation
  Increasing power does not reduce error
Error floor depends on BdTs

## Slide 6: ISI Effects
Delay spread exceeding a symbol time causes ISI (self interference).
ISI leads to irreducible error floor
  Increasing signal power increases ISI power
ISI requires that Ts>>Tm (Rs<<Bc)
0
Tm
1
2
3
4
5
Ts

## Slide 7: Main Points
In fading Ps is a random variable, characterized by average value, outage, or combined outage/average
  Fading greatly increases average Ps .
  Alternate Q function approach simplifies Ps calculation, especially its average value in fading (Laplace Xfm).
  In fast/slow fading, outage is due to shadowing, probability of error then averaged over fast fading pdf
Doppler spread only impacts differential modulation causing an irreducible error floor at low data rates
Delay spread causes irreducible error floor or imposes rate limits
Need to combat flat and frequency-selective fading
  Focus of the remainder of the course