## Slide 1: EE359 – Lecture 19 Outline
Review of Last Lecture
OFDM FFT Implementation
OFDM Design Issues
Introduction to Spread Spectrum
ISI and Interference Rejection

## Slide 2: Review of Last Lecture
Multicarrier Modulation: breaks data into N substreams (B/N<Bc); Substream modulated onto separate carriers
Overlapping substreams
  Minimum substream separation is BN=1/TN
Discrete implementation of MCM uses DSP
  Use cyclic prefix to make linear convolution circular
x
cos(2pf0t)
x
cos(2pfNt)
S
R bps
R/N bps
R/N bps
QAM
Modulator
QAM
Modulator
Serial
To
Parallel
Converter

## Slide 3: FFT Implementation of OFDM
  Use IFFT at TX to modulate symbols on each subcarrier
  Cyclic prefix makes linear convolution of channel circular, so no interference between FFT blocks in RX processing
  Reverse structure (with FFT) at receiver
x
cos(2pfct)
R bps
QAM
Modulator
Serial
To
Parallel
Converter
IFFT
X0
XN-1
x0
xN-1
Add cyclic
prefix and
Parallel
To Serial
Convert
D/A
TX
x
cos(2pfct)
R bps
QAM
Modulator
FFT
Y0
YN-1
y0
yN-1
Remove
cyclic
prefix and
Serial to
Parallel
Convert
A/D
LPF
Parallel
To Serial
Convert
RX

## Slide 4: OFDM Design Issues
Timing/frequency offset:
  Impacts subcarrier orthogonality; self-interference
Peak-to-Average Power Ratio (PAPR)
  Adding subcarrier signals creates large signal peaks
MIMO/OFDM
  Apply OFDM across each spatial dimension
  Can adapt across space, time, and frequency
Different fading across subcarriers
  Mitigate by precoding (fading inversion), coding across subcarriers, and adaptative loading over time

## Slide 5: Intro. to Spread Spectrum
Modulation that increases signal BW
  Mitigates or coherently combines ISI
  Mitigates narrowband interference/jamming
  Hides signal below noise (DSSS) or makes it hard to track (FH)
  Also used as a multiple access technique
Two types
  Frequency Hopping: (Heddy Lamar)
    Narrowband signal hopped over wide bandwidth
  Direction Sequence: (ITT-NJ)
    Modulated signal multiplied by faster chip sequence

## Slide 6: Direct Sequence Spread Spectrum
Bit sequence modulated by chip sequence
Spreads bandwidth by large factor (G)
Despread by multiplying by sc(t) again (sc(t)=1)
Mitigates ISI and narrowband interference
s(t)
sc(t)
Tb=KTc
Tc
S(f)
Sc(f)
1/Tb
1/Tc
S(f)*Sc(f)
2

## Slide 7: ISI and Interference Rejection
Narrowband Interference Rejection (1/K)
Multipath Rejection (Autocorrelation r(t))
S(f)
S(f)
I(f)
S(f)*Sc(f)
Info. Signal
Receiver Input
Despread Signal
I(f)*Sc(f)
S(f)
aS(f)
S(f)*Sc(f)[ad(t)+b(t-t)]
Info. Signal
Receiver Input
Despread Signal
brS’(f)

## Slide 8: Main Points
OFDM efficiently implemented using IFFTs/FFTs
  Block size depends on data rate relative to delay spread
OFDM challenges: PAPR; timing/frequency offset, MIMO
Subcarrier fading degrades OFDM performance
  Compensate through precoding (channel inversion), coding across subcarriers, or adaptation
4G Cellular, Wimax, 802.11n all use OFDM+MIMO
Spread spectrum increases signal bandwidth above that required for information transmission
  Benefits: ISI/interference rejection, multiuser technique