## Slide 1: EE359 – Lecture 6 Outline
Review of Last Lecture
Signal Envelope Distributions
Average Fade Duration
Markov Models
Wideband Multipath Channels
Scattering Function
Multipath Intensity Profile
Doppler Power Spectrum

## Slide 2: Review of Last Lecture
  For fn~U[0,2p], rI(t),rQ(t) zero mean, WSS, with
  Uniform AoAs in Narrowband Model
  In-phase/quad comps have zero cross correlation and
  PSD is maximum at the maximum Doppler frequency
    PSD used to generate simulation values
Decorrelates over roughly
half a wavelength

## Slide 3: Signal Envelope Distribution
CLT approx. leads to Rayleigh distribution (power is exponential)
When LOS component present, Ricean distribution is used
Measurements support Nakagami distribution in some environments
  Similar to Ricean, but models “worse than Rayleigh”
  Lends itself better to closed form BER expressions

## Slide 4: Level crossing rate and Average Fade Duration
LCR: rate at which the signal crosses a fade value
AFD: How long a signal stays below target R/SNR
  Derived from LCR
For Rayleigh fading
  Depends on ratio of target to average level (r)
  Inversely proportional to Doppler frequency
R
t1
t2
t3

## Slide 5: Markov Models for Fading
Model for fading dynamics
  Simplifies performance analysis
Divides range of fading power into discrete regions Rj={g: Aj  g < Aj+1}
  Aj s and # of regions are functions of model
Transition probabilities (Lj is LCR at Aj):
A0
A1
A2
R0
R1
R2

## Slide 6: Wideband Channels
Individual multipath components resolvable
True when time difference between components exceeds signal bandwidth
t
t
Narrowband
Wideband

## Slide 7: Scattering Function
Fourier transform of c(t,t) relative to t
Typically characterize its statistics, since c(t,t) is different in different environments
Underlying process WSS and Gaussian, so only characterize mean (0) and correlation
Autocorrelation is Ac(t1,t2,Dt)=Ac(t,Dt)
Statistical scattering function:
t
r
s(t,r)=FDt[Ac(t,Dt)]

## Slide 8: Multipath Intensity Profile
Defined as Ac(t,Dt=0)= Ac(t)
  Determines average (TM ) and rms (st) delay spread
  Approximate max delay of significant m.p.
Coherence bandwidth Bc=1/TM
  Maximum frequency over which Ac(Df)=F[Ac(t)]>0
  Ac(Df)=0 implies signals separated in frequency by Df will be uncorrelated after passing through channel
t
Ac(t)
TM
t
f
Ac(f)
0
Bc

## Slide 9: Doppler Power Spectrum
Sc(r)=F[Ac(t=0,Dt)]= F[Ac(Dt)]
Doppler spread Bd is maximum doppler for which Sc (r)=>0.
Coherence time Tc=1/Bd
  Maximum time over which Ac(Dt)>0
  Ac(Dt)=0 implies signals separated in time by Dt will be uncorrelated after passing through channel
r
Sc(r)
Bd

## Slide 10: Main Points
Fading distribution depends on environment
  Rayleigh, Ricean, and Nakagami all common
Average fade duration determines how long a user is in continuous outage (e.g. for coding design)
Markov model approximates fading dynamics.
Scattering function characterizes rms delay and Doppler spread. Key parameters for system design.
Delay spread defines maximum delay of significant multipath components. Inverse is coherence BW
Doppler spread defines maximum nonzero doppler, its inverse is coherence time