## Slide 1: EE359 – Lecture 9 Outline
Linear Modulation Review
Linear Modulation Performance in AWGN
Q-Function representations
Probability of error in fading
Outage probability
Average Ps (Pb)

## Slide 2: Review of Last Lecture
Capacity in Flat-Fading: g known at TX/RX
    Optimal Rate and Power Adaptation
    Channel Inversion and Truncated Inversion
      Received SNR constant; Capacity is Blog2(1+s) above an outage level associated with truncation
Capacity of ISI channels
  Water-filling of power over freq; or time and freq.
Capacity of ISI Channels
1
g
g0
g
Waterfilling

## Slide 3: Passband Modulation Tradeoffs
Want high rates, high spectral efficiency, high power efficiency, robust to channel, cheap.
Amplitude/Phase Modulation (MPSK,MQAM)
  Information encoded in amplitude/phase
  More spectrally efficient than frequency modulation
  Issues: differential encoding, pulse shaping, bit mapping.
Frequency Modulation (FSK)
  Information encoded in frequency
  Continuous phase (CPFSK) special case of FM
  Bandwidth determined by Carson’s rule (pulse shaping)
  More robust to channel and amplifier nonlinearities
Our focus

## Slide 4: Amplitude/Phase Modulation
Signal over ith symbol period:
  Pulse shape g(t) typically Nyquist
  Signal constellation defined by (si1,si2) pairs
  Can be differentially encoded
  M values for (si1,si2)log2 M bits per symbol
Ps depends on
  Minimum distance dmin (depends on gs)
  # of nearest neighbors aM
  Approximate expression:

## Slide 5: Alternate Q Function Representation
Traditional Q function representation
  Infinite integrand
  Argument in integral limits
New representation (Craig’93)
  Leads to closed form solution for Ps in PSK
  Very useful in fading and diversity analysis

## Slide 6: Linear Modulation in Fading
In fading gs and therefore Ps random
Performance metrics:
  Outage probability: p(Ps>Ptarget)=p(g<gtarget)
  Average Ps , Ps:
  Combined outage and average Ps (next lecture)

## Slide 7: Outage Probability
Probability that Ps is above target
Equivalently, probability gs below target
Used when Tc>>Ts
Ps
Ps(target)
Outage
Ts
t or d

## Slide 8: Average Ps
Expected value of random variable Ps
Used when Tc~Ts
Error probability much higher than in AWGN alone
Alternate Q function approach:
  Simplifies calculations (Get a Laplace Xfm)
Ps
Ps
Ts
t or d

## Slide 9: Main Points
Linear modulation more spectrally efficient but less robust than nonlinear modulation
Ps approximation in AWGN:
  Alternate Q function representation simplifies calculations
In fading Ps is a random variable, characterized by average value, outage, or combined outage/average
Outage probability based on target SNR in AWGN.
Fading greatly increases average Ps .