## Slide 1
CIRCUITS 1
DEVELOP TOOLS FOR THE ANALYSIS AND DESIGN OF
BASIC LINEAR ELECTRIC CIRCUITS

## Slide 2
A FEW WORDS ABOUT ANALYSIS
USING MATHEMATICAL MODELS

## Slide 3
BASIC STRATEGY USED IN ANALYSIS

## Slide 4
MATHEMATICAL ANALYSIS
DEVELOP A SET OF MATHEMATICAL
EQUATIONS THAT REPRESENT THE CIRCUIT
- A MATEMATICAL MODEL -
LEARN HOW TO SOLVE THE MODEL TO
DETERMINE HOW THE CIRCUIT WILL BEHAVE
IN A GIVEN SITUATION
THIS COURSE TEACHES THE BASIC TECHNIQUES
TO DEVELOP MATHEMATICAL MODELS FOR
ELECTRIC CIRCUITS
THE MATHEMATICS CLASSES - LINEAR ALGEBRA,
DIFFERENTIAL EQUATIONS- PROVIDE THE TOOLS
TO SOLVE THE MATHEMATICAL MODELS
THE MODELS THAT WILL BE DEVELOPED HAVE
NICE MATHEMATICAL PROPERTIES.
IN PARTICULAR THEY WILL BE LINEAR WHICH
MEANS THAT THEY SATISFY THE PRINCIPLE OF
SUPERPOSITION
FOR THE FIRST PART WE WILL BE EXPECTED
TO SOLVE SYSTEMS OF ALGEBRAIC EQUATIONS
LATER THE MODELS WILL BE DIFFERENTIAL
EQUATIONS OF THE FORM

## Slide 5
LOW DISTORTION POWER AMPLIFIER
ELECTRIC CIRCUIT IS AN INTERCONNECTION OF ELECTRICAL COMPONENTS
TYPICAL LINEAR
CIRCUIT

## Slide 6
BASIC CONCEPTS
LEARNING GOALS
System of Units: The SI standard system; prefixes
Basic Quantities: Charge, current, voltage, power and energy
Circuit Elements: Active and Passive

## Slide 7
http://physics.nist.gov/cuu/index.html

## Slide 10
SI DERIVED BASIC ELECTRICAL UNITS

## Slide 11
ONE AMPERE OF CURRENT CARRIES ONE COULOMB OF CHARGE EVERY SECOND.
VOLT IS A MEASURE OF ENERGY PER CHARGE.
TWO POINTS HAVE A VOLTAGE DIFFERENCE OF ONE VOLT IF ONE COULOMB OF CHARGE
GAINS ONE JOULE OF CHARGE WHEN IT IS MOVED FROM ONE POINT TO THE OTHER.
OHM IS A MEASURE OF THE RESISTANCE TO THE FLOW OF CHARGE.
THERE IS ONE OHM OF RESISTENCE IF IT IS REQUIRED ONE VOLT OF ELECTROMOTIVE FORCE
TO DRIVE THROUGH ONE AMPERE OF CURRENT
IT IS REQUIRED ONE WATT OF POWER TO DRIVE ONE AMPER OF CURRENT AGAINST AN
ELECTROMOTIVE DIFFERENCE OF ONE VOLTS

## Slide 12
CURRENT AND VOLTAGE RANGES

## Slide 13
Strictly speaking current is a basic quantity and charge is derived. However,
physically the electric current is created by a movement of charged particles.
What is the meaning of a negative value for q(t)?
PROBLEM SOLVING TIP
IF THE CHARGE IS GIVEN DETERMINE THE CURRENT BY
DIFFERENTIATION
IF THE CURRENT IS KNOWN DETERMINE THE CHARGE BY
INTEGRATION
A PHYSICAL ANALOGY THAT HELPS VISUALIZE ELECTRIC
CURRENTS IS THAT OF WATER FLOW.
CHARGES ARE VISUALIZED AS WATER PARTICLES

## Slide 14
EXAMPLE
EXAMPLE
FIND THE CHARGE THAT PASSES
DURING IN THE INTERVAL 0<t<1
FIND THE CHARGE AS A FUNCTION OF TIME
And the units for the charge?...
Units?

## Slide 15
Here we are given the
charge flow as function
of time.
DETERMINE THE CURRENT
To determine current we
must take derivatives.
PAY ATTENTION TO
UNITS

## Slide 16
CONVENTION FOR CURRENTS
IT IS ABSOLUTELY NECESSARY TO INDICATE
THE DIRECTION OF MOVEMENT OF CHARGED
PARTICLES.
THE UNIVERSALLY ACCEPTED CONVENTION IN
ELECTRICAL ENGINEERING IS THAT CURRENT IS
FLOW OF POSITIVE CHARGES.
AND WE INDICATE THE DIRECTION OF FLOW
FOR POSITIVE CHARGES
-THE REFERENCE DIRECTION-
A POSITIVE VALUE FOR
THE CURRENT INDICATES
FLOW IN THE DIRECTION
OF THE ARROW (THE
REFERENCE DIRECTION)
A NEGATIVE VALUE FOR
THE CURRENT INDICATES
FLOW IN THE OPPOSITE
DIRECTION THAN THE
REFERENCE DIRECTION
THE DOUBLE INDEX NOTATION
IF THE INITIAL AND TERMINAL NODE ARE
LABELED ONE CAN INDICATE THEM AS
SUBINDICES FOR THE CURRENT NAME
POSITIVE CHARGES
FLOW LEFT-RIGHT
POSITIVE CHARGES
FLOW RIGHT-LEFT

## Slide 17
This example illustrates the various ways
in which the current notation can be used

## Slide 18
CONVENTIONS FOR VOLTAGES
ONE DEFINITION FOR VOLT
TWO POINTS HAVE A VOLTAGE DIFFERENTIAL OF
ONE VOLT IF ONE COULOMB OF CHARGE GAINS
(OR LOSES) ONE JOULE OF ENERGY WHEN IT
MOVES FROM ONE POINT TO THE OTHER
IF THE CHARGE GAINS
ENERGY MOVING FROM
a TO b THEN b HAS HIGHER
VOLTAGE THAN a.
IF IT LOSES ENERGY THEN
b HAS LOWER VOLTAGE
THAN a
DIMENSIONALLY VOLT IS A DERIVED UNIT
VOLTAGE IS ALWAYS MEASURED IN A RELATIVE FORM AS THE VOLTAGE DIFFERENCE
BETWEEN TWO POINTS
IT IS ESSENTIAL THAT OUR NOTATION ALLOWS US TO DETERMINE WHICH POINT
HAS THE HIGHER VOLTAGE

## Slide 19
THE + AND - SIGNS
DEFINE THE REFERENCE
POLARITY
IF THE NUMBER V IS POSITIVE POINT A HAS V
VOLTS MORE THAN POINT B.
IF THE NUMBER V IS NEGATIVE POINT A HAS
|V| LESS THAN POINT B
POINT A HAS 2V MORE
THAN POINT B
POINT A HAS 5V LESS
THAN POINT B

## Slide 20
THE TWO-INDEX NOTATION FOR VOLTAGES
INSTEAD OF SHOWING THE REFERENCE POLARITY
WE AGREE THAT THE FIRST SUBINDEX DENOTES
THE POINT WITH POSITIVE REFERENCE POLARITY
WHAT ENERGY IS REQUIRED TO MOVE 120[C] FROM
POINT B TO POINT A IN THE CIRCUIT?
THE CHARGES MOVE TO A POINT WITH HIGHER
VOLTAGE -THEY GAINED (OR ABSORBED) ENERGY
WHICH POINT HAS THE
HIGHER VOLTAGE?
THE VOLTAGE
DIFFERENCE
IS 5V

## Slide 21
EXAMPLE
A CAMCODER BATTERY PLATE CLAIMS THAT
THE UNIT STORES 2700mAHr AT 7.2V.
WHAT IS THE TOTAL CHARGE AND ENERGY
STORED?
CHARGE
THE NOTATION 2700mAHr INDICATES THAT
THE UNIT CAN DELIVER 2700mA FOR ONE
FULL HOUR
TOTAL ENERGY STORED
THE CHARGES ARE MOVED THROUGH A 7.2V
VOLTAGE DIFFERENTIAL
ENERGY AND POWER
2[C/s] PASS
THROUGH
THE ELEMENT
EACH COULOMB OF CHARGE LOSES 3[J]
OR SUPPLIES 3[J] OF ENERGY TO THE
ELEMENT
THE ELEMENT RECEIVES ENERGY AT A
RATE OF 6[J/s]
THE ELECTRIC POWER RECEIVED BY THE
ELEMENT IS 6[W]
HOW DO WE RECOGNIZE IF AN ELEMENT
SUPPLIES OR RECEIVES POWER?
IN GENERAL

## Slide 22
PASSIVE SIGN CONVENTION
POWER RECEIVED IS POSITIVE WHILE POWER
SUPPLIED IS CONSIDERED NEGATIVE
A CONSEQUENCE OF THIS CONVENTION IS THAT
THE REFERENCE DIRECTIONS FOR CURRENT AND
VOLTAGE ARE NOT INDEPENDENT -- IF WE
ASSUME PASSIVE ELEMENTS
IF VOLTAGE AND CURRENT
ARE BOTH POSITIVE THE
CHARGES MOVE FROM
HIGH TO LOW VOLTAGE
AND THE COMPONENT
RECEIVES ENERGY --IT IS
A PASSIVE ELEMENT
GIVEN THE REFERENCE POLARITY
IF THE REFERENCE DIRECTION FOR CURRENT
IS GIVEN
THIS IS THE REFERENCE FOR POLARITY
REFERENCE DIRECTION FOR CURRENT
EXAMPLE
THE ELEMENT RECEIVES 20W OF POWER.
WHAT IS THE CURRENT?
SELECT REFERENCE DIRECTION BASED ON
PASSIVE SIGN CONVENTION

## Slide 23
S2
S1
We must examine the voltage across the component
and the current through it
A
A’
B
B’
UNDERSTANDING PASSIVE SIGN CONVENTION

## Slide 24
CHARGES RECEIVE ENERGY.
THIS BATTERY SUPPLIES ENERGY
CHARGES LOSE ENERGY.
THIS BATTERY RECEIVES THE ENERGY
WHAT WOULD HAPPEN IF THE CONNECTIONS ARE REVERSED
IN ONE OF THE BATTERIES?

## Slide 25
DETERMINE WHETHER THE ELEMENTS ARE SUPPLYING OR RECEIVING POWER
AND HOW MUCH
WHEN IN DOUBT LABEL THE TERMINALS
OF THE COMPONENT
SUPPLIES POWER
RECEIVES POWER

## Slide 26
SELECT VOLTAGE REFERENCE POLARITY
BASED ON CURRENT REFERENCE DIRECTION
SELECT HERE THE CURRENT REFERENCE DIRECTION
BASED ON VOLTAGE REFERENCE POLARITY
WHICH TERMINAL HAS HIGHER VOLTAGE AND WHICH IS THE CURRENT FLOW DIRECTION

## Slide 27
P1 = 12W
P2 = 36W
P3 = -48W
IMPORTANT: NOTICE THE POWER BALANCE IN THE CIRCUIT
COMPUTE POWER ABDORBED OR SUPPLIED BY EACH ELEMENT

## Slide 28
CIRCUIT ELEMENTS
PASSIVE ELEMENTS
INDEPENDENT SOURCES
VOLTAGE
DEPENDENT
SOURCES
CURRENT
DEPENDENT
SOURCES

## Slide 29
EXERCISES WITH DEPENDENT SOURCES
DETERMINE THE POWER SUPPLIED BY THE DEPENDENT SOURCES
TAKE VOLTAGE POLARITY REFERENCE
TAKE CURRENT REFERENCE DIRECTION

## Slide 30
POWER ABSORBED OR SUPPLIED BY EACH
ELEMENT
NOTICE THE POWER BALANCE
USE POWER BALANCE TO COMPUTE Io
POWER BALANCE