## Slide 1: Analog and Digital Filter Design Review Signals
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Continuous or analog signals
Discrete-time signals
Basic analog signals
Basic discrete signals
Quantized signals
Digital signals
Causal signals
Random signals
Representation of signals in MATLAB

## Slide 3: What is a signal?
A signal is a physical quantity, or quality, which conveys information
Example: voice of my friend is a signal which causes me to perform certain actions or react in a particular way
My friend's voice is called an excitation
My action or reaction is called a response

## Slide 4: What is signal processing?
The conversion from excitation to response is called signal processing
A typical reason for signal processing is to eliminate or reduce an undesirable signal
We convert the original signal into a form that is suitable for further processing
One fundamental representation of a signal is as a function of at least one independent variable

## Slide 5: What is a waveform
The variation of the signal value as a function of the independent variable is called a waveform
The independent variable often represents time
We define a signal as a function of one independent variable that contains information about the behavior or nature of a phenomenon
We assume that the independent variable is time even in cases where the independent variable is a physical quantity other than time

## Slide 6: Continuous or analog signals
Continuous signal is a signal that exists at every instant of time
In the jargon of the trade, a continuous signal is often referred to as continuous time or analog
The independent variable is a continuous variable
Continuous signal can assume any value over a continuous range of numbers

## Slide 7: Discrete-time signals
A signal defined only for discrete values of time is called a discrete-time signal or simply a discrete signal
Discrete signal can be obtained by taking samples of an analog signal at discrete instants of time
Digital signal is a discrete-time signal whose values are represented by digits

## Slide 8: What is sampling?
Sampling is capturing a signal at an instant in time
Sampling means taking amplitude values of the signal at certain time instances
Uniform sampling is sampling every T units of time
Sampling frequency or sampling rate
time step or sample interval

## Slide 9: Sinusoidal signal
Frequency in Hertz (Hz)
Amplitude
Phase in radian (rad)
Time in seconds (s)

## Slide 10: MATLAB code for sine signal
Xs = 1.8;
fs = 10;
fi = pi/3;
t1 = -0.1;
tstep = 0.01;
t2 = 0.2;
t = t1:tstep:t2;
x = Xs*sin(2*pi*fs*t+fi);
plot(t, x)
xlabel('t')
ylabel('x_s')
title('x_s(t) = X_s sin(2 \pi f_s t + \phi_s)')
grid on

## Slide 11: Advanced MATLAB code
Xs = 1.8;
fs = 10;
fi = pi/3;
t1 = -0.1;
t2 = 0.2;
t = [t1, t2];
x = inline('Xs*sin(2*pi*fs*t+fi)','t','Xs','fs','fi');
fplot(x,t,2e-3,1,'-',Xs,fs,fi)
xlabel('t'); ylabel('x_s'); grid on
title('x_s(t) = X_s sin(2 \pi f_s t + \phi_s)')

## Slide 12: Exponential signal
x = inline('Xe*exp(b*t)','t','Xe','b');
Xe = 0.8;
b = -0.5;
t1 = 0;
t2 = 8;
t = [t1, t2];
fplot(x,t,2e-3,1,'-',Xe,b)
xlabel('t')
ylabel('x_e')
title('x_e(t) = X_e e^{b t}')
grid on

## Slide 13: Unit step signal
x = inline('t>0', 't');
t1 = -2;
t2 = 6;
t = [t1, t2];
fplot(x, t)
xlabel('t')
ylabel('u')
title('Unit step signal')
axis([t -0.1 1.1])

## Slide 14: Pulse signal
x = inline('(1/e)*((t>0)&(t<=e))','t','e');
e = 1/100;
t1 = -1;
t2 = 5;
t = [t1, t2];
fplot(x,t,1e-5,1000,'-',e)
set(gca,'FontSize',16)
xlabel('t')
ylabel('p_\epsilon(t)')
axis([t -0.1 1.1/e])
title('Pulse function, \epsilon = 1/100')

## Slide 15: Unit impulse signal (Dirac delta)

## Slide 16: Causal signals
A signal is causal if it is zero for t < 0
Causal signals are readily created by multiplying any continuous signal by the unit step signal
The instant when the signal begins is called the starting time
We usually take the starting time to be zero

## Slide 17: Causal signals in MATLAB
B = 0.02;
a = 0.1;
f = 0.53;
phi = 3*pi/4;
t = -5:0.05:10;
x = B^a*exp(-a*t).*sin(...
2*pi*f*t+phi);
xu = x.*(t>0);
u = (t>0);
plot(t,x,t,u,t,xu)
ylabel('x(t)')
xlabel('t (s)')
text(0,1.2,'u(t)')
text(-4,-1.1,'x(t)')
text(5,-.6,'x(t)*u(t)')
axis([t(1) t(end) -1.5 1.5])

## Slide 18: Discrete-time signal – Sequence
A sequence (discrete-time signal, discrete signal, data sequence, or sample set) is a collection of ordered samples
In practical applications we process finite-length sequences
The existing sequence is often a sampled version of a continuous signal

## Slide 19: Sinusoidal sequence
Amplitude
Phase in radian (rad)
Sample index
Period

## Slide 20: Exponential sequence
Xe = 0.8;
a = 0.75;
k1 = 0;
k2 = 10;
k = k1:k2;
x = Xe*a.^k;
stem(k, x)
xlabel('k')
ylabel('x_e')
title('x_{e,k} = X_e a^k')

## Slide 21: Unit step sequence
k1 = -5;
k2 = 10;
k = k1:k2;
x = (k>=0);
stem(k, x)
xlabel('k')
ylabel('u_k')
title('Unit step sequence')
axis([k1 k2 -0.1 1.1])

## Slide 22: Unit impulse sequence
k1 = -5;
k2 = 10;
k = k1:k2;
x = (k==0);
stem(k, x)
xlabel('k')
ylabel('\delta_k')
title('Unit impulse sequence')
axis([k1 k2 -0.1 1.1])

## Slide 23: Causal sequence
A sequence that is nonzero only over a finite interval of indices is called a finite-length sequence
A sequence whose samples are zero-valued for negative indices is causal
Anti-causal sequence can have nonzero samples only for negative indices

## Slide 24: Causal sequences in MATLAB
B = 0.94; a = 0.1; f = 0.32;
k = -10:1:20;
x = (B.^k).*cos(2*pi*f*k);
u = (k>=0);
ux = x.*u;
subplot(3,1,1)
stem(k,u,'g')
ylabel('u_k','FontSize',14)
axis([k(1) k(end) -2 2])
subplot(3,1,2)
stem(k,x,'b')
ylabel('x_k','FontSize',14)
subplot(3,1,3)
stem(k,ux,'r')
ylabel('x_k u_k','FontSize',14)
xlabel('k')
axis([k(1) k(end) -2 2])

## Slide 25: Quantized signal
The purpose of sampling a continuous signal is to transmit, store, or process a limited number of samples that are represented by a limited number of digits
By using fewer digits we attain faster transmission and smaller storage requirements for the information
We utilize the quantized samples rather than the true samples of infinite accuracy

## Slide 26: Choice of digits for quantization
Choice of digits for quantization should be done properly: in transmitting, storing, and processing we prefer less digits
With too small a number of digits we can lose information from the original signal
Two opposing requirements must be satisfied:
  Minimize number of digits to facilitate the signal transmission or storing, and
  Maximize number of digits to keep the quantization error as low as necessary in order to preserve the information

## Slide 27: Digital signal in MATLAB
t = 0:30;
x = 0.2+2*sin(0.245*t+0.15);
d = 0.5;
xq = d*round(x/d);
plot(t,x)
hold on
stem(t,xq,'r')
hold off
ylabel('x(t), x_q(kT)')
xlabel('t')
legend('analog signal',...
'digital (quantized)')

## Slide 28: Deterministic and random signal
Signal that can be described by an explicit mathematical form is deterministic
Deterministic signal can be periodic or aperiodic
Periodic signal consists of a basic shape of finite duration that is replicated infinitely
Signal that cannot be described in an explicit mathematical form is called random, also known as nondeterministic or stochastic

## Slide 29: Random signal in MATLAB
xk = 0:1:50;
x = rand(size(k));
m = mean(x);
s = std(x);
stem(k,x)
hold on
plot([k(1) k(end)],…
[m m],'r',...
[k(1) k(end)],…
[s s],'g')
hold off
xlabel('k')
ylabel('x_k')
ytick = [0 s m 1]; set(gca,'YTick',ytick)
legend('random seq',…
'mean','std')
title('Uniformly distributed samples')

## Slide 30: Random signal in MATLAB
k = 0:1:50;
x = randn(size(k));
m = mean(x);
s = std(x);
stem(k,x)
hold on
plot([k(1) k(end)],…
[m m],'r',…
[k(1) k(end)],…
[s s],'g')
hold off
xlabel('k')
ylabel('x_k')
legend('random seq',…
'mean','std')
ytick = sort([-2 s m 2]);
set(gca,'YTick',ytick)
title('Normally distributed samples')

## Slide 31: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/