## Slide 1: Analog and Digital Filter Design System transfer function, poles and zeros, pole-zero pairing
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Transfer function in s domain
Transfer function in z domain
Pole-zero-gain representation
Examples
MATLAB freqs, roots
MATLAB freqz, zplane, tf2pzk, tf2sos

## Slide 3: Transfer function
Continuous-time LTI systems

## Slide 4: What is transfer function?
We consider a relaxed, single-input, single-output, continuous-time LTI system described by means of a linear constant-coefficients differential equation
We assume a causal excitation – input
Transfer function, H(s), is the ratio of the output Laplace transform, Y(s), and the input Laplace transform, X(s)

## Slide 5: H(s) is a rational function in s
Transfer function is a ratio of two polynomials in the complex frequency s
For s = j, H(s) is the frequency response of the LTI system
Many properties of LTI systems can be closely associated with the characteristics of the transfer function in the s-plane

## Slide 6: Poles and zeros
Roots of the transfer function denominator A(s) are called the poles
We compute the poles from the equation A(s) = denominator(H(s)) = 0
Roots of the transfer function numerator B(s) are called the zeros
We obtain the zeros from the equation B(s) = numerator(H(s)) = 0

## Slide 7: Pole-zero representation
zeros
poles
Polynomials A(s) and B(s) have real coefficients, so zeros and poles must be real or occur in complex conjugate pairs

## Slide 8: First-order sections & biquads
the first-order transfer function
the second-order transfer function
Systems described by the first-order transfer function we call first-order sections
A system characterized by the second-order transfer function we call a biquadratic section or biquad
Any transfer function can be expressed as a product of first-order and second-order transfer functions, so any LTI system can be resolved into first-order sections and biquads

## Slide 9: freqs
A = [1 0.4 1]; B = [0.2 0.3 1]; w = 0.1:0.01:10; H = freqs(B,A,w); M = abs(H); P = angle(H); subplot(2,1,1); loglog(w,M); grid; ylabel('Magnitude'); title('H = freqs(B,A,w)'); subplot(2,1,2); semilogx(w,P); grid; ylabel('Phase (rad)'); xlabel('\omega');

## Slide 10: roots
A = [1 0.4 1];
B = [0.2 0.3 1];
z = roots(B);
p = roots(A);
plot(real(z),imag(z),'ro',… real(p),imag(p),'bx')
axis([-1 0.1 -2.5 2.5])
xlabel('real part')
ylabel('imaginary part')
legend('zeros','poles')

## Slide 11: Quality factor (Q-factor)
complex-conjugate pairs

## Slide 12: Complex pole-zero pair
To reduce the sensitivity of a transfer function with respect to deviations of the coefficient values, it is preferable to represent the transfer function by a product of the first-order and second-order transfer functions

## Slide 13: Lowpass transfer function

## Slide 14: Highpass transfer function

## Slide 15: Bandpass transfer function

## Slide 16: Bandreject transfer function

## Slide 17: Allpass transfer function

## Slide 18: Amplitude equalizer

## Slide 19: Pole-zero pairing
Decomposition of the numerator and the denominator into products of constant terms, and the first-order and the second-order functions
Constructing the first-order and the second-order rational functions by pairing the numerator and denominator terms
Frequently used: pairing the poles with higher Q-factors with zeros that are as close as possible to the poles

## Slide 20: Pole-zero pairing criteria
Maximal dynamic range: a ratio of (a) the maximum magnitude response computed over the whole frequency range to (b) the minimum magnitude response in the passband
Maximal signal-to-noise ratio
Minimal sensitivity

## Slide 21: Transfer function
Discrete-time LTI systems

## Slide 22: What is transfer function?
We consider a relaxed, single-input, single-output, discrete-time LTI system described by means of a linear constant-coefficients difference equation
We assume a causal excitation – input
Transfer function, H(z), is the ratio of the output z transform, Y(z), and the input z transform, X(z)

## Slide 23: H(z) is a rational function in z
Transfer function is a ratio of two polynomials in the complex variable z
For z = ej, H(z) is the frequency response of the LTI system
Many properties of LTI systems can be closely associated with the characteristics of the transfer function in the z-plane

## Slide 24: Poles and zeros
Roots of the transfer function denominator A(z) are called the poles
We compute the poles from the equation A(z) = denominator(H(z)) = 0
Roots of the transfer function numerator B(z) are called the zeros
We obtain the zeros from the equation B(z) = numerator(H(z)) = 0

## Slide 25: Pole-zero representation
zeros
poles
Polynomials A(z) and B(z) have real coefficients, so zeros and poles must be real or occur in complex conjugate pairs

## Slide 26: First-order sections & biquads
the first-order transfer function
the second-order transfer function
Systems described by the first-order transfer function we call first-order sections
A system characterized by the second-order transfer function we call a biquadratic section or biquad
Any transfer function can be expressed as a product of first-order and second-order transfer functions, so any LTI system can be resolved into first-order sections and biquads

## Slide 27: H(z) can be expressed in terms of z-1
A quotient of two polynomials is called a rational function and the highest power in the polynomials is called the order of the rational function
This presentation is preferred in the DSP community

## Slide 28: freqz
B = [0.0093 -0.0123 0.0232 -0.0172 0.0233 -0.0124 0.0094] A = [1 -4.312 8.5888 -9.8704 6.8602 -2.7272 0.4865] freqz(B,A)

## Slide 29: zplane
B = [0.0093 -0.0123 0.0232 -0.0172 0.0233 -0.0124 0.0094] A = [1 -4.312 8.5888 -9.8704 6.8602 -2.7272 0.4865] zplane(B,A) legend('zeros','poles')

## Slide 30: tf2zpk
B = [0.0093 -0.0123 0.0232 -0.0172 0.0233 -0.0124 0.0094] A = [1 -4.312 8.5888 -9.8704 6.8602 -2.7272 0.4865] [z,p,k] = tf2zpk(B,A)

## Slide 31: tf2sos
B = [0.0093 -0.0123 0.0232 -0.0172 0.0233 -0.0124 0.0094] A = [1 -4.312 8.5888 -9.8704 6.8602 -2.7272 0.4865] sos = tf2sos(B,A)

## Slide 32: Quality factor (Q-factor)
complex-conjugate pairs

## Slide 33: Lowpass transfer function

## Slide 34: Highpass transfer function

## Slide 35: Bandpass transfer function

## Slide 36: Bandreject transfer function

## Slide 37: Allpass transfer function

## Slide 38: Pole-zero pairing
Decomposition of the numerator and the denominator into products of constant terms, the first-order and the second-order polynomials
Constructing the first-order and the second-order rational functions by pairing the numerator and denominator terms
Frequently used: pairing the poles with higher a with zeros that are as close as possible to those poles

## Slide 39: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/