## Slide 1: Analog and Digital Filter Design Specification of an analog filter
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Analog filter specification
Analog filter design steps
Analog filter classification
Sensitivity
Optimum cascading sequence
Examples
MATLAB cheb1ord, cheb1ap

## Slide 3: What are analog filters?
Analog filters are frequency-selective circuits that are used to amplify or attenuate a single sinusoidal signal component or a portion of the signal frequency spectrum
Passband is a range of frequencies in which the sinusoidal signals are amplified or passed without considerable attenuation
Stopband is a frequency range in which the sinusoidal signals are significantly attenuated
Specification is the required minimum and maximum of attenuation or amplification, along with corresponding edge frequencies of passbands and stopbands

## Slide 4: What is analog filter design?
Analog filter design is a process in which we construct an electrical circuit that meets the given specification
Design starts with the specification and it consists of four basic steps:
  approximation
  realization
  study of imperfections
  implementation
There is an infinite number of circuits that meet the specification; therefore, the filter design is by no means unique

## Slide 5: Classic filter design
If requirements are
not met, realization step (new circuit) or the approximation step must be redone

## Slide 6: Specification example
Assume we want to design an analog lowpass filter that passes signals over the range 0 ≤ f ≤ Fp and attenuates signals for f ≥ Fs > Fp
Range 0 ≤ f ≤ Fp is passband, and f ≥ Fs is stopband; Fp is passband edge frequency and Fs is stopband edge frequency
We require that attenuation in passband must not exceed Ap dB in stopband should be no less than As dB
Ap is maximum passband attenuation As is minimum stopband attenuation
Four quantities that specify lowpass filter S = {Fp, Fs, Ap, As} is the lowpass specification

## Slide 7: Approximation step
Approximation step: we construct filter transfer function H(s), which is a rational function in the complex frequency s
Attenuation approximation function, simply attenuation, A(f) = −20 log10|H(j2f)|, must satisfy the specification S

## Slide 8: Realization step
Realization step is the process of converting the transfer function into a circuit (sometimes called the realization)
Designers are interested in realizations which are economical, simple, cheap, with small noise and distortion, and with high dynamic range and which are not seriously affected by small changes in the element values (tolerances, temperature and humidity variations, aging drift)
Numerical values of the elements are calculated from the transfer function

## Slide 9: Study of imperfections
In practice, the filter is implemented with nonideal elements
Designer must accomplish the study of imperfections which includes tolerance analysis and study of parasitics
If specification can be met only with high-precision expensive components, then the designer has to choose another transfer function and reevaluate realization or approximation steps

## Slide 10: Implementation step
In the implementation step a device called the product prototype, also called the implementation, is constructed and tested
Cost of the mass production depends on the type of components, packaging, methods of manufacturing, testing, and tuning
The best implementation is a device with no need for tuning
If the requirements are not met, then the realization step (new circuit) or the approximation step must be redone

## Slide 11: Analog filter classification (1)
Lowpass filter passes signals over the range 0 ≤ f ≤ Fp but attenuates signals for f ≥ Fs > Fp
Highpass filter passes signals for f ≥ Fp but attenuates signals over the range 0 ≤ f ≤ Fs < Fp
Bandpass filter passes signals for Fp1 ≤ f ≤ Fp2 but attenuates signals for 0 ≤ f ≤ Fs1 < Fp1 and f ≥ Fs2 > Fp2
Bandreject or bandstop filter passes signals for 0 ≤ f ≤ Fp1 < Fs1 and f ≥ Fp2 > Fs2 but attenuates signals over the range Fs1 ≤ f ≤ Fs2

## Slide 12: Analog filter classification (2)
Allpass filter or phase equalizer passes signals without attenuation and shapes the phase response
Lowpass-notch filter rejects signals at frequencies f ≈ fz but passes signals at high frequencies (f >> fz) with some attenuation
Highpass-notch filter rejects sinusoidal signals at frequencies f ≈ fz but passes signals at low frequencies (f << fz) with some attenuation
Amplitude equalizer or bump filter slightly amplifies or attenuates signals over a range of frequencies

## Slide 13: Decomposition of transfer functions
To reduce the sensitivity of a transfer function with respect to deviations of the element values and to simplify the tuning process of the filter, it is preferable to realize the filter by a cascade of the first-order and second-order filter sections
Cascade approach consists of realizing each of the sections by an appropriate circuit and connecting these circuits in cascade
Overall transfer function is expressed as a product of first-order and second-order functions

## Slide 14: Optimum cascading sequence
After a transfer function is decomposed into first-order and second-order functions designer has to choose the optimal cascading sequence
For the maximal dynamic range, the optimal sequence of the second-order filter sections is the sequence in which the preceding section has lower Q-factor than the following section
If the input signal contains an undesired signal with very large amplitude, this signal has to be filtered out by the very first section, which should have a transfer function zero at the frequency of the undesired signal

## Slide 15: Production yield
Before the filter is manufactured, the effects of manufacturing tolerances and component imperfections have to be analyzed
Designer should predict variations of the filter performances and the production yield
Yield is the ratio of (a) the number of manufactured filters satisfying the specification to (b) the total number of manufactured filters
High yield is desirable for profitability

## Slide 16: Sensitivity
The simplest way to predict the yield is to use the concept of sensitivity assuming that the component changes are small
Single-parameter relative sensitivity of a function
Expected relative variation in function
Example: If a sensitivity is 1, then a 1% change in the variable (component value) will cause a 1% change in the function; when a sensitivity is zero, then any change in variable will not affect the function

## Slide 17: Upper limit of the relative variation
Worst-case method gives the absolute relative variation assuming that all changes are at their extreme
Schoeffler criterion method is closer to the variation obtained by statistical computations
Monte Carlo method relies on extensive simulation of the filter realization (circuit) with randomly chosen element values

## Slide 18: Example specification and design
Fp = 3400; Fs = 5000;
Ap = 1; As = 20;
[n, Wn] = cheb1ord(Fp, Fs, Ap, As, 's')
[z,p,k] = cheb1ap(n, Ap);
Q = (-abs(p)./(2*real(p)));
w = round(abs(p)*(2*pi*Fp));
D1 = [1 w(1)/Q(1) w(1)^2];
D2 = [1 w(2)/Q(2) w(2)^2];
N1 = w(1)^2; N2 = w(2)^2;
D = conv(D1,D2);
N = 10^(-Ap/20)*conv(N1,N2);
Fplot = 6000;
f = 0:Fplot/200:Fplot;
H = freqs(N,D,2*pi*f);
M = -20*log10(abs(H));
subplot(2,1,1)
plot(f,M,[0 Fp Fp],[Ap Ap As],'r--',… [Fs Fs Fplot],[0 As As],'r--')
xlabel('f (Hz)'); ylabel('A (dB)')
subplot(2,1,2)
drawschematic(0,0,4,5,8,'b')

## Slide 19: Example sensitivity analysis
Pole magnitudes and Q-factors increased by 10%: stopband specification violated
Pole magnitudes and Q-factors decreased by 10%: passband specification violated
See the Matlab script Lecture06sens.m

## Slide 20: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/