## Slide 1: Analog and Digital Filter Design Classical analog filter design: Op amp and RLC realizations
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Classification of analog filters
Active RC filters
Low Q-, Medium Q-, High Q-factor filters
Album of op amp RC biquads
Example biquad design
MATLAB script Lecture08lplq.m

## Slide 3: Analog filter realizations
After having accomplished the approximation step, the filter transfer function is known
Next, the designer must choose a realization, that is, an electric circuit
Analog filters can be classified on the basis of their constituent components

## Slide 4: Classification of analog filters
Passive RLC filters
Operational amplifier RC filters (op amp active RC filters)
Switched-capacitor (SC) filters
Operational transconductance amplifier (OTA) filters
Current-conveyor (CC) filters
Microwave filters
Electromechanical filters
Crystal filters

## Slide 5: Passive RLC filters
Consist of passive macrocomponents: resistors, capacitors, and inductors (coils and transformers)
Do not require a power supply
Drawbacks:
  Exhibit a significant passband loss,
  Inductors cannot be miniaturized
Practical at frequencies up to a few hundred MHz
Important in deriving realizations of some active filters, such as active RC, OTA, and current-conveyor filters

## Slide 6: Active RC filters
Can be reduced in size and weight, especially when implemented as integrated circuits
Manufacturing can be automated with high production yield
Made out of resistors, capacitors, and operational amplifiers
Disadvantages:
  Require a power supply
  Output signal can be distorted if the input signal is too large
  Extra noise is generated in active devices
Operate over the frequency rage from 0.1 Hz to 500 kHz

## Slide 7: Op amp active RC filters
Realizations

## Slide 8: Classification of biquadratic realizations
Low Q-factor realizations (Q < 2) exhibit no problems with tolerances, no need for tuning, minimal number of passive components, and only one operational amplifier
Medium Q-factor realizations (2 < Q < 20) selected on the basis of minimum gain-sensitivity product, simple tuning, minimal number of passive components, and only one operational amplifier
High Q-factor realizations (20 < Q) require two operational amplifiers, sensitivities are lower than the sensitivity of single-amplifier biquads

## Slide 9: Lowpass low-Q-factor

## Slide 10: Example biquad design

## Slide 11
% Given a second-order lowpass transfer function we identify
fp = 2300;
wp = 2*pi*fp;
Qp = 1.2;
% Choose K < 1
K = 0.6;
% Choose 0.1 < P=R3/R1 < 10
P = 3.3865;
% Choose C4
nano = 10^(-9); Cx = 3.3*nano;
C4 = Cx;
% Compute element values
C2 = 2*Qp^2*Cx*(1+(1+P^2)/(2*P));
R1 = 1/(wp*Cx*Qp*(1+P));
R3 = P*R1; R11 = R1/K; R12 = R1/(1-K);
% Generate transfer function in terms of element values
num = R12;
den = [(C2*C4*R11*R12*R3) (C4*R11*R12+C4*R11*R3+C4*R12*R3) (R11+R12)];
f = 0:80:8000; w = i*2*pi*f; H = num./polyval(den,w);
subplot(2,1,1); drawlplq(0,0,4,5,10,'b')
subplot(2,1,2); plot(f,abs(H))

## Slide 12: Highpass Low-Q-factor

## Slide 13: Bandpass low-Q-factor

## Slide 14: Bandreject low-Q-factor

## Slide 15: Allpass low-Q-factor

## Slide 16: Lowpass medium-Q-factor

## Slide 17: Highpass medium-Q-factor

## Slide 18: Bandpass medium-Q-factor

## Slide 19: Bandreject medium-Q-factor

## Slide 20: Allpass medium-Q-factor

## Slide 21: Lowpass notch medium-Q-factor

## Slide 22: Highpass notch medium-Q factor

## Slide 23: Lowpass high-Q-factor

## Slide 24: Highpass high-Q-factor

## Slide 25: Bandpass high-Q-factor

## Slide 26: Bandreject high-Q-factor

## Slide 27: Lowpass notch high-Q-factor

## Slide 28: Highpass notch high-Q-factor

## Slide 29: General-purpose realization
KHN filter (Kerwin-Huelsman-Newcomb)

## Slide 30: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/