## Slide 1: Analog and Digital Filter Design Classical digital filter design
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
What is digital filter?
Classic digital filter design
Digital filter classification
Decomposition of transfer function
Transfer function types
Classification of realizations
Example design and comparison of realizations

## Slide 3: What is digital filter?
Digital filter is a discrete-time system that alters the spectral information contained in some discrete-time signal x producing a new discrete-time signal y
Sampled signals are represented digitally as sequences of numbers
We consider linear time-invariant systems used for smoothing, predicting, differentiating, integrating, and separating signals, as well as for removing noise from the signal x
We define a DSP system as a system used for digital signal processing

## Slide 4: Sampling frequency
Key quantity of a digital filter is its sampling frequency also called the sampling rate
We assume that a sequence of numbers xk is obtained from equally spaced samples of some quantity x(t), where k is an integer and t is a continuous variable
Typically, t represents time or space distance

## Slide 5: Typical processing

## Slide 6: Transfer function
Frequency response
Magnitude response

## Slide 7: Magnitude response

## Slide 8: Digital filter design
Digital filter design is a process in which we construct a digital hardware or a program (software) that meets the given specification
The design starts with the specification, and it consists of four basic steps: approximation, realization, study of imperfections, and implementation

## Slide 9: Classic digital filter design
If requirements are
not met, realization step or approximation step must be redone
There is an infinite number of systems that meet the specification; therefore, the filter design is by no means unique

## Slide 10: Digital frequency
The frequency f = 1/2 is called the Nyquist frequency

## Slide 11: Passband and stopband
Passband is a range of frequencies in which sinusoidal sequences are amplified or passed without considerable attenuation
Stopband is a frequency range in which sinusoidal sequences are significantly attenuated
Specification is the required minimum and maximum of attenuation or amplification, along with corresponding edge frequencies of passbands and stopbands

## Slide 12: Specification example
Assume we want to design a digital lowpass filter that passes signals over the range 0 ≤ f ≤ Fp < ½ and attenuates signals for f ≥ Fs > Fp
Range 0 ≤ f ≤ Fp < ½ is passband, and f ≥ Fs is stopband; Fp is passband edge frequency and Fs is stopband edge frequency
We require that attenuation in passband must not exceed Ap dB in stopband should be no less than As dB
Ap is maximum passband attenuation As is minimum stopband attenuation
Four quantities that specify lowpass filter S = {Fp, Fs, Ap, As} is the lowpass specification
f < ½

## Slide 13: Approximation step
Approximation step: we construct filter transfer function H(z), which is a rational function in the complex frequency z
Attenuation approximation function, simply attenuation, A(f) = −20 log10|H(ej2f)|, must satisfy the specification S

## Slide 14: Realization step
Realization step is the process of converting the transfer function into a block diagram or program (software); this block diagram or software is called the realization
Designers are interested in realizations which are economical, simple, and cheap, with short wordlength and high dynamic range
Numerical values of the coefficients are calculated from the transfer function

## Slide 15: Study of imperfections
In practice, the filter is implemented with nonideal elements
Designer must accomplish the study of imperfections which includes filter coefficient quantization effects, product quantization effects (uncorrelated roundoff or truncation noise) and dynamic range constrains
If the specification can be satisfied only with high-precision coefficients and very long wordlength, then the designer has to choose another transfer function and reevaluate the realization or approximation step

## Slide 16: Implementation step
In the implementation step a device called the product prototype, also called the implementation, is constructed and tested
Cost of the mass production depends on the type of components, packaging, methods of manufacturing and testing
If the requirements are not met, then the realization step (new digital filter network or new software program) or the approximation step must be redone

## Slide 17: Digital filter classification (1)
Lowpass filter passes signals over the range 0 ≤ f ≤ Fp but attenuates signals for f ≥ Fs > Fp
Highpass filter passes signals for f ≥ Fp but attenuates signals over the range 0 ≤ f ≤ Fs < Fp
Bandpass filter passes signals for Fp1 ≤ f ≤ Fp2 but attenuates signals for 0 ≤ f ≤ Fs1 < Fp1 and f ≥ Fs2 > Fp2
Bandreject or bandstop filter passes signals for 0 ≤ f ≤ Fp1 < Fs1 and f ≥ Fp2 > Fs2 but attenuates signals over the range Fs1 ≤ f ≤ Fs2
f < ½

## Slide 18: Digital filter classification (2)
Allpass filter or phase equalizer passes signals without attenuation and shapes the phase response
Lowpass-notch filter rejects signals at frequencies f ≈ fz but passes signals at high frequencies (f >> fz) with some attenuation
Highpass-notch filter rejects sinusoidal signals at frequencies f ≈ fz but passes signals at low frequencies (f << fz) with some attenuation
Amplitude equalizer slightly amplifies or attenuates signals over a range of frequencies
f < ½

## Slide 19: Decomposition of transfer function
Any higher-order transfer function can be expressed as a product of the first-order and the second-order transfer functions
The first-order and the second-order transfer functions are realized separately
The transfer function is realized by cascading these low-order filter section
The cascade design is attractive:
  Filter design is straightforward
  Case study for selecting the appropriate low-order filter realizations is facilitated
  Effort for quantization analyzes is simplified

## Slide 20: Optimum cascading sequence
After a transfer function is decomposed into first-order and second-order functions designer has to choose the optimal cascading sequence
For the maximal dynamic range, the optimal sequence of the second-order filter sections is the sequence in which the preceding section has lower Q-factor than the following section

## Slide 21: Pole-zero representation
zeros
poles
Polynomials A(z) and B(z) have real coefficients, so zeros and poles must be real or occur in complex conjugate pairs

## Slide 22: First-order sections & biquads
the first-order transfer function
the second-order transfer function
Systems described by the first-order transfer function we call first-order sections
A system characterized by the second-order transfer function we call a biquadratic section or biquad
Any transfer function can be expressed as a product of first-order and second-order transfer functions, so any LTI system can be resolved into first-order sections and biquads

## Slide 23: Quality factor (Q-factor)
complex-conjugate pairs

## Slide 24: Lowpass transfer function

## Slide 25: Highpass transfer function

## Slide 26: Bandpass transfer function

## Slide 27: Bandreject transfer function

## Slide 28: Allpass transfer function

## Slide 29: Pole-zero pairing
Decomposition of the numerator and the denominator into products of constant terms, the first-order and the second-order polynomials
Constructing the first-order and the second-order rational functions by pairing the numerator and denominator terms
Frequently used: pairing the poles with higher a with zeros that are as close as possible to those poles

## Slide 30: Pole-zero pairing criteria
Maximal dynamic range: a ratio of (a) the maximum magnitude response computed over the whole frequency range to (b) the minimum magnitude response in the passband
The choice of the scaling factors of the first-order and the second-order sections is called the gain distribution; there exist procedures for optimizing the gain distribution for maximal dynamic range

## Slide 31: Classification of realizations
on the basis of filter structure

## Slide 32: Digital filter classification
Direct-form I
Direct-form II (or Direct canonic)
Cascade
Parallel
Wave digital (WDF)
Parallel-of-two-allpass
Ladder
Filters based on structural passivity

## Slide 33: Direct-form filters
Direct-form I filters are realized directly from the difference equation. The filter coefficients can be identified directly from the difference equation describing the filter. Can be implemented in a straightforward and efficient way.
Direct-form II filters, also referred to as direct canonic filters, have the minimal number of delays. By definition, a canonic realization is a realization with the minimal number of delays.

## Slide 34: Cascade and parallel filters
Cascade filters are realized as a cascade of first-order and second-order sections. Each section can be realized as direct-form I, direct-form II, or any other type.
Parallel filters are realized as a parallel connection of first-order and second-order sections, that is, the outputs of the lower-order sections are connected to an adder. Each section can be realized as direct-form I, direct-form II, or any other type.

## Slide 35: Wave digital filters and parallel-of-two-allpass filters
Wave digital filters are derived from microwave filters. Analysis and design of these filters rely on microwave theory and techniques.
Parallel-of-two-allpass filters are realized as a parallel connection of two allpass filters, each filter being realized as a cascade of allpass lower-order sections (first-order and second-order sections). They have identical properties as wave digital filters.

## Slide 36: Ladder filters and filters based on structural passivity
Ladder filters may be preferable to direct, cascade, or parallel realizations in filter applications where coefficient sensitivity is of primary concern. Its implementation nearly doubles the computational cost.
Filters based on structural passivity are based on the zero sensitivity of magnitude response to multiplier coefficients at the frequencies of maximal magnitude response. The key property of these filters is that the magnitude response cannot be larger than 1, and small changes of the filter coefficient values only change the frequency at which the maximum occurs.

## Slide 37: Direct-form I realization

## Slide 38: Direct-form II realization

## Slide 39: Transposed direct-form II

## Slide 40: Ansari-Liu allpass biquad type B

## Slide 41: Example design
Comparison of realizations

## Slide 42: Specification

## Slide 43: Cascade realization
The poles are purely imaginary, so some multipliers in the feedback branch do not exist.
The transfer function zeros are on the unit circle, which enables the realization of a feedforward branch with only one multiplier with a non-unity coefficient.
The cascade realization with the reduced number of multipliers can realize a transfer functions of any order – odd or even.

## Slide 44: Parallel realization
The residues of the transfer function are either purely real or purely imaginary. In that case, the feedforward branches of the second-order sections of parallel realization (formed by decomposing the transfer function into partial fractions) have only one multiplier with a nonzero coefficient.
Some multipliers in the feedback branches do not exist.

## Slide 45: Parallel connection of two allpass filters
This realization exists only for the odd-order transfer functions. Each of the allpass filters is realized as a cascade connection of first-order and second-order allpass sections.
The parallel-of-two-allpass realization is the most economical realization for half-band filters, because the second-order filter sections are realized with only one multiplier.
This realization has larger magnitude response sensitivity in the stopband when compared to the cascade or parallel realization.

## Slide 46: Wave digital filters
Exists for the odd-order transfer functions. It is based on a set of four-port building blocks derived from the microwave theory.
Wave digital realizations exhibit the same features as parallel-of-two-allpass realizations.

## Slide 47: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/